Attached is mls900. This is a more refined version of mls800. You may have noticed the accelerated speed 3 in mls800 is not the same for in and out. One of those keys was setting accelerated speed 2 instead of speed 3.

Looking at your notes I see there is a problem not knowing what is supposed to happen, not knowing what a keypress is, confusion about totally different actions mixed on the same layer and confusion over what the words on the oled mean. So here is some stuff to better explain. These versions are meant to demonstrate ideas. Some totally different and conflicting ideas might be on the same layer.

These are the mls900 keymaps. A general description for each layer is the text before the layer keymap is shown.

/* KC_NO means no keycode, ie do nothing */

/* [_BASE] One shot strides and also standard out of box mouse wheel action */

[_BASE] // encoder press goto _ALTERNATE1

TURN_0, KC_NO, KC_NO, // counter zero
GOTO_0, KC_NO, STRIDE_1, // goto postion 0, kc_no, set stride to 1
ENC_U, KC_WH_U, ENC_STRIDE_INC, // 1 shot u click stride x, reg. wheel,inc stride
ENC_D, KC_WH_D, ENC_STRIDE_DEC // 1 shot d click stride x, reg. Wheel, inc stride

/* [_ALTERNATE1] QMK accelerated mouse wheel action
The SPD_1_x, SPD_2_x, SPD_3_x keys set three speed ranges.
Speed is currently set at compile time. Position counter n/a. */

[_ALTERNATE1] = LAYOUT(TO(_ALTERNATE2), // encoder press goto _ALTERNATE2

TURN_0, KC_NO, KC_NO, // counter zero
GOTO_0, KC_NO, KC_NO, // goto postion 0
SPD_1_U, SPD_2_U, SPD_3_U, // up @ spd 1, up @ spd 2, up @ spd 3
SPD_1_D, SPD_2_D, SPD_3_D // dn @ spd 1, dn @ spd 2, dn @ spd 3

/* [_ALTERNATE2] MLS mouse wheel speed control. The encoder sets stride
while keys are used for up and down at stride distance. */

[_ALTERNATE2] = LAYOUT(TO(_LED_SETTINGS), // encoder press goto _LED_SETTINGS
TURN_0, KC_NO, STRIDE_1, // counter 0, kc_no, set stride to 1
GOTO_0, KC_NO, STRIDE_1, // goto postion 0, kc_no, set stride to 1
MLS_WHLU, MLS_WHLU, MLS_WHLU, // all keys do up
MLS_WHLD, MLS_WHLD, MLS_WHLD // all keys do dn

/* [_LED_SETTINGS] LED animation setting layer */
[_LED_SETTINGS] = LAYOUT(TO(_STANDBY), // encoder press goto _STANDBY
RM_NEXT, KC_NO, RM_TOGG, // Next RGB animation, kc_no, Animation on/off
KC_NO, KC_NO, KC_NO,
RM_VALU, RM_HUEU, RM_SPDU, // intensity up, color hue up, amim speed up
RM_VALD, RM_HUED, RM_SPDD // intensity dn, color hue dn, amim speed dn

/* [_STANDBY] A standby layer where keys and encoder turns do nothing */
[_STANDBY] = LAYOUT(MSG_READY, // encoder press goto _BASE
MSG_STBY, MSG_STBY, MSG_STBY,
MSG_STBY, MSG_STBY, MSG_STBY,
MSG_STBY, MSG_STBY, MSG_STBY,
MSG_STBY, MSG_STBY, MSG_STBY

The following are mouse wheel settings that are set at compile time. These control the timing and other settings. The 3 speed accelerated settings are in here.

/* Mousekey speed control */
// #define MK_MOMENTARY_ACCEL
#define MK_3_SPEED
#define MK_COMBINED
#define MOUSEKEY_WHEEL_DELAY 10 // Time between wheel movements in default mode.
#define MOUSEKEY_WHEEL_INTERVAL 60 // Time between wheel movements in default mode.
#define MOUSEKEY_WHEEL_TIME_TO_MAX	20 // Time until maximum scroll speed is reached
#define MK_W_INTERVAL_UNMOD 10 // default is 40
#define MK_W_INTERVAL_0 360 // MS_ACL0 , default 360
#define MK_W_INTERVAL_1 120 // MS_ACL1 , default 120
#define MK_W_INTERVAL_2 20 // MS_ACL2 , default 360

/*
Accelerated (default mouse):
These are the default values if not modified like above.
MOUSEKEY_WHEEL_DELAY	10	Delay between pressing a wheel key and wheel movement
MOUSEKEY_WHEEL_INTERVAL	80	Time between wheel movements
MOUSEKEY_WHEEL_DELTA	1	Wheel movement step size (leave this be!)
MOUSEKEY_WHEEL_MAX_SPEED	8	Maximum number of scroll steps per scroll action
MOUSEKEY_WHEEL_TIME_TO_MAX	40	Time until maximum scroll speed is reached
The following does not apply for our use being scroll only.
(cursor) Holding movement keys accelerates the cursor until it reaches its maximum speed.
(cursor) MOUSEKEY_DELAY	10	Delay between pressing a movement key and cursor movement
(cursor) MOUSEKEY_INTERVAL	20	Time between cursor movements in milliseconds
(cursor) MOUSEKEY_MOVE_DELTA	8	Step size
(cursor) MOUSEKEY_MAX_SPEED	10	Maximum cursor speed at which acceleration stops
(cursor) MOUSEKEY_TIME_TO_MAX	30	Time until maximum cursor speed is reached
*/